## Slide 1: Reinforcement Learning for Parrot Mambo Minidrone Attitude Control
Mücahid Rıdvan KAPLAN
Mehmet SAKARYA
Computer Engineering & Hacettepe University
07 Jun, 2024

## Slide 2: Introduction
Flight control systems generally composed of;
  Position & altitude control
  Speed control
  Navigation control
  Attitude control
PID (Proportional-Integral-Derivative) controllers are used due to their simplicity, stability and real time response capabilities.
While PID systems adequate for lots of operations, it has some challenges.
Notes: We worked with the drone control systems. These systems composed of different control algorithms. We aimed to control the attitude controller.
This controller is made by using the PID controller . However, PID controllers have some limitations.

## Slide 3: PID Algorithms
Limitations in Varying Environments
  PID controllers struggle with unknown dynamics such as wind and voltage sag.
Adaptability Requirement
  Next-gen systems need to adapt to mutable dynamics and varying environments.
Performance in Stable Environments
  PID controllers perform close to ideally in stable conditions.
Notes: PID controllers sensitive to varying environment conditions. Therefore, at the different environment, climate or mission conditions flight perfromance fall seriously.

## Slide 4: Why RL Algorithms Used
  Advantages
  Self-Learning: RL agents learn control strategies through trial and error in a simulated environment, reducing manual tuning.
  Adaptability: RL agents can adapt to changing environments and new tasks by continuously learning from experience.
Notes: When we look at why we used RL algorithms, Their advantages are self learning mechanism and adaptability. Reinforcement learning is an machine learning subfield and hence it has capable to learn by training. And this training make it adapts to varying environment conditions easily.

## Slide 5: Training Algorithms
1- Deep Deterministic Policy Gradient Algorithm (DDPG)
Model-free, online, off-policy reinforcement learning method
DDPG agent is an actor-critic reinforcement learning agent
Actor: takes state and returns corresponding actions
Critic: takes observation and action as input and return corresponding expectation of the long term reward
Notes: One of the most common used method is DDPG algorithm. It is an continuous system and therefore usable in the UAV’s
It consists of the actor and critic networks. Actor network takes the states and returns actions.
Critic network gets the state and action as input and returns the best action. This best action evaluated with the long term rewards.

## Slide 7
2- Proximal Policy Optimization (PPO)
Model-free, online, on-policy, policy gradient reinforcement learning algorithm
Working process is
  Decide step size α
  Construct a circle with radius α (trust region)
  Once having the best point, determine the direction
  Repeat until the optimal point is reached
Notes: PPO algorithm also have actor-critic networks and it is continuous space agent.
Its working principle is based on small steps in the trusted region. It’s direction is determined when the best point is found in the circular. Once best point is found new trust region appears and again struggles to find best point. This process continue untill optimal,target, point is found.

## Slide 8
Notes: DDPG PPO actor critic figürleri alınacak

## Slide 9: Literature-1 Overview
Specific Focus
  Deep dive into the accuracy and precision of attitude control using intelligent flight controllers trained with RL.
Training Environment
  Introduction of GymFC, an OpenAI Environment, designed for training intelligent flight control systems.
RL Application
  Application of RL algorithms for attitude control and their potential transfer to physical hardware.
Koch, William, et al. "Reinforcement learning for UAV attitude control." ACM Transactions on Cyber-Physical Systems 3.2 (2019): 1-21.

## Slide 10: Literature-1 Results

## Slide 11: Literature-2 Overview
Specific Focus
  Controlling the quadcopter by using DDPG & D4PG RL algorithms.
Training Environment
  GymFC for training intelligent flight control of quadcopter.
RL Application
  Comparative analysis of the performance of DDPG &D4PG
  algorithms in terms of reward generation, actor loss, and critic performance.

## Slide 12: Literature-2 Results

## Slide 13: Simulink Environment of Project
Notes: This is the our Project environment at Simulink platform. Each block responsible for different tasks.
Signal Editor : It generates position and attitude commands
Sensors : It includes the model of sensors such as IMU on the quadcopter
Flight Control System : It is responsible for position and attitude control. Here, we will perform attitude control using RL (Reinforcement Learning)
Environment : It includes gravity, air temperature, speed of sound, pressure, air density, and magnetic field
Airframe : It contains the nonlinear model of the quadcopter
Visualization: : It facilitates logging and scoping of commands, control signals, and states, it contains also workspace and Simulink 3D animation.

## Slide 14: Flight Controller Block
Notes: This is the flight control system block that we focused one.
The orange blocks are normally controlled with PID controller. However, we added inside these blocks RL agents.
Our plan was firstly run the environment with PID controlling blocks. And this worked fine
After then changed one of the blocks with RL agent and trained. We did not change both of these blocks simultaneously. If it is done simultaneously agent training itself wrongly due to the two unknown dynamic struct

## Slide 15: Roll & Pitch RL Agent
Observation States
Roll angle error
Pitch angle error
Integral of roll angle error
Integral of pitch angle error
Estimated Roll body rate
Estimated Pitch body rate
Action States
Tau Pitch
Tau Roll
r1(t) = e−(0.5|θr −θ|+0.5|φr −φ|)
r2(t) = −(0.3(θr − θ)2 + 0.3(φr − φ)2 + 0.15(|p|+|q|) + 0.1(τθ 2 + τφ2))
r3(t) = −((θr − θ)2 + (φr − φ)2)
r4(t) = −(0.5(θr − θ) + 0.5(φr − φ))
Notes: This is the agent and its environment block for roll and pitch attitude control.
Input parameters are observation, reward Function and flag. the output is the action.

## Slide 16
r1(t) = e−(0.5|θr −θ|+0.5|φr −φ|)
Notes: Normalde rewardün maximize etmesi beklenir. Osilasyon belirli steplede reward
Average reward 10 tanesinin ortalaması
Reward function :
<roll error ve pitch error 0.5 . Bunların weight değerleri 2side 0.5 ikiside aynı oranda ödül + ceza.
>
<1 bölü e üzeri denklem… Bu hata sıfıra gittikçe reward 1 e yaklaşacak demek. Hata sonsuza giderse reward 0 olacak . Exponential terim klullanrak hataya 0 ve 1 arasına sınırlandırk [değer]
Maksimum step 2000 yapıldı, bu bize ne sağladı<
Her bir step maksimum 1 olabilir, bu yüzden her bir episode maksimum 2000 değerinni alır>
Training stopping criteria 1500 olarak seçildi. {hiçbir zaman 900 ün üzerine geçemedik ve anlık osilasyonlar oldu }

## Slide 17
r2(t) = −(0.3(θr − θ)2 + 0.3(φr − φ)2 + 0.15(|p|+|q|) + 0.1(τθ 2 + τφ2))
Notes: Katsayı ve üssel ifadelerden dolayı değişen hata oranlarında episoode reward değerinde hızlı yükseliş ve alçalışlar oluşmakta.
Başlangıçta < >
Steady State Yakınında <>
Sistem kararlı değildi roll ekseni etrafında dönmekte.

## Slide 18: Trainig Results
r3(t) = −((θr − θ)2 + (φr − φ)2)
Notes: Bu rewar function kullanarak değerlendirmeler

## Slide 19
r4(t) = −(0.5(θr − θ) + 0.5(φr − φ))

## Slide 20: Contributions
  In this project we aimed to make yaw controller and roll-pitch controller with RL agent distinctly, and this study is not inside any literatüre that we have seen.
  These training showed to possibilities of this idea.
  Different algorithmic parameters and observation states lead to different outputs, seen at results.
Notes:   Yapılabilirliği üzerine bir çalışma yürütüldü istenilen performasnların sergilenemediği görüldü. Training yapılamadığı fakat drone üzerinde nonlinear sistemde RL çalışması yoktu ve biz bunu denemiş olduk.
  Algoritma learning rate observation sattae training times:5 saat vb.
  Training episode related with zaman
Oldukça uzun bir zam

## Slide 21: References
[1] N. Bernini, M. Bessa, R. Delmas, A. Gold, E. Goubault, R. Pennec, S. Putot, and F. Sillion, “Reinforcement learning with formal performance metrics for quadcopter attitude control under non-nominal contexts,Engineering Applications of Artificial Intelligence, vol. 127, p. 107090, 2024. [2] E. Bøhn, E. M. Coates, S. Moe, and T. A. Johansen, “Deep reinforcement learning attitude control of fixed-wing uavs using proximal policy opti- mization,” in 2019 international conference on unmanned aircraft systems (ICUAS). IEEE, 2019, pp. 523–533. [3] U. H. Ghouri, M. U. Zafar, S. Bari, H. Khan, and M. U. Khan, “Attitude control of quad-copter using deterministic policy gradient algorithms (dpga),” in 2019 2nd International Conference on Communication, Com- puting and Digital systems (C-CODE). IEEE, 2019, pp. 149–153. [4] W. Koch, R. Mancuso, R. West, and A. Bestavros, “Reinforcement learning for uav attitude control,” ACM Transactions on Cyber-Physical Systems, vol. 3, no. 2, pp. 1–21, 2019. [5] Y. Zhen, M. Hao, and W. Sun, “Deep reinforcement learning attitude control of fixed-wing uavs,” in 2020 3rd International Conference on Unmanned Systems (ICUS). IEEE, 2020, pp. 239–244.
[6] Reinforcement Learning Toolbox Documentation (mathworks.com)

## Slide 22
Thanks for Listening.