## Slide 1: Reinforcement Learning for Parrot Mambo Minidrone Attitude Control
Mücahid Rıdvan KAPLAN
Mehmet SAKARYA
Computer Engineering & Hacettepe University
09 May, 2024

## Slide 2: Introduction
  Control algorithm of the quadcopter for roll - pitch and yaw angles are made by using the PID control systems.
  PID control system dynamics is not stable for unknown environments
  In this project RL algorithm approaches planned instead of the PID controller by using 2 different RL agents.
  2 different agent will be used for xy controller and z controller for 2 stages
  Creating a new reward function is harder than the implementing that agent.
Notes: Our Project is the controlling of quadcopter angles with RL agent instead of PID controller.
Because PID system is not stable for unknown environment.
We planned to use the DDPG and PPO agents for xy controller and z controller.
Why we chose these two agents ?
Before the Project proposal presentation we searched related literatures and noticed these two agent performance is better than other agents. Therefore we focused these.
We are planning to new reward function that is unlike the literature ones to find an better performance, if possible.

## Slide 3: Deep Deterministic Policy Gradient (DDPG) Algorithm
Model-free, online, off-policy reinforcement learning method
DDPG agent is an actor-critic reinforcement learning agent
Actor: takes state and returns corresponding actions
Critic: takes observation and action as input and return corresponding expectation of the long term reward
Notes: Actor-critic 🡪 searches for an optimal policy that maximizes the expected cumulative long-term reward.
How DDPG (Deep Deterministic Policy Gradient) Algorithms works in reinforcement learning ? | by Amaresh Marekar | Medium
Actor : decides by selecting actions based on the current policy (policy is modelled)
explores the action space to maximize reward
Critic : value function , evaluates the actions
estimates the value of actions by providing feedback on their performance

## Slide 4: Trust Region Policy Optimization (TRPO) Algorithm
Model-free, online, on-policy, policy gradient reinforcement learning algorithm
Working process is
  Decide step size α
  Construct a circle with radius α (trust region)
  Once having the best point, determine the direction
  Repeat until the optimal point is reached

## Slide 5: Proximal Policy Optimization (PPO) Algorithm
3 main advantages:
  Simplicity
  Stability
  Sample efficiency
Easier to implement and tune while performing well in challenging environments.
Instead of making big changes all at once, PPO encourages small and gradual improvements.
Notes: “Proximal” means staying close to the original style
“Policy Optimization” is about finding better strategies.

## Slide 6: Article 1 – RL for UAV attitude control
Specific Focus
  Deep dive into the accuracy and precision of attitude control using intelligent flight controllers trained with RL.
Training Environment
  Introduction of GymFC, an OpenAI Environment, designed for training intelligent flight control systems.
RL Application
  Application of RL algorithms for attitude control and their potential transfer to physical hardware.
Koch, William, et al. "Reinforcement learning for UAV attitude control." ACM Transactions on Cyber-Physical Systems 3.2 (2019): 1-21.
Notes: As an alternative way to the supervised learning method to make intelligent flight control system is using the RL algorithms as this projects main aim.
This Project focuses on intelligent flight controller with RL algorithms to make better accuracy and precision of attitude control.

## Slide 7: Environment

## Slide 8: Results

## Slide 9: Article 2 – Attitude Control of Quad-copter using DPGA
Specific Focus
  Controlling the quadcopter by using DDPG & D4PG RL algorithms.
Training Environment
  GymFC for training intelligent flight control of quadcopter.
RL Application
  Comparative analysis of the performance of DDPG &D4PG algorithms in terms of reward generation, actor loss, and critic performance.
Ghouri, Usama Hamayun, et al. "Attitude control of quad-copter using deterministic policy gradient algorithms (DPGA)." 2019 2nd International Conference on Communication, Computing and Digital systems (C-CODE). IEEE, 2019.

## Slide 10: DDPG & D4PG Algorithms
DDPG: Deep Deterministic Policy Gradient
D4PG : Distributed Distributional Deterministic Policy Gradient
Extended and enhanced algorithm of DDPG for improving :
  Stability
  Sample efficiency
  Performance

## Slide 11: Angle Stabilization Performances

## Slide 12: Simulink Environment of Project
Notes: This is the our Project environment at Simulink platform. Each block responsible for different tasks.
Signal Editor : AC command are creted
Sensors : ……………………………….
Flight Control System : ………………………………….
Environment : ………………………………
Airframe : ………………………………

## Slide 13: Flight Control System Block
Notes: This is the flight control system block that we focused one.
The orange blocks are normally controlled with PID controller. However, we added inside these blocks RL agents.
Our plan was firstly run the environment with PID controling blocks. And this worked fine
After then changed one of the blocks with RL agent and trained . We did not change both of these blocks simultaneously. If it is done simultaneously agent training itself wrongly due to the two unknown
dynamic struct

## Slide 14: Roll & Pitch PID Attitude Controller
Notes: This is PID control block for attitude controller for quadcopter.
…………………………………….

## Slide 15: Roll & Pitch RL Agent
Observation States
Roll angle reference
Pitch angle reference
Estimated Roll angle
Estimated Pitch angle
Estimated Roll body rate
Estimated Pitch body rate
Action States
Tau Pitch
Tau Roll
  = -clip(sum(||/3 ,0,1)
Notes: This is the agent and its environment block.
Input parameters are observation, reward Function and flag. the output is the action.

## Slide 16: Yaw PD Attitude Controller
Notes: This is PD control block for yaw attitude controller for quadcopter.
…………………………………….

## Slide 17: Yaw RL Agent
Observation States
Yaw angle reference
Estimated Yaw angle
Estimated Yaw body rate
Action State
Tau Yaw
  = -clip(sum(||/3 ,0,1)
Notes: This is the agent and its environment block.
Input parameters are observation, reward Function and flag. the output is the action.

## Slide 18: Agent Training
Notes: This is our first output of trained RL agent.
This is not an true for us for this because we only focused to obtain some data from the agent block.
This is trained with 6 episodes. This is not enough and episodes will be more and more to obtain better training agent.
This agent is negative because of the reward function which is multiplied by -1.
While the actions close to the desired positions, reward will be around 0.

## Slide 19: Command Generation for Task

## Slide 20: Future Plans & Progress
  Solving training problems
  Limiting the observation and action blocks
  Implementing 2 different DDPG and PPO algorithms together
  Agent configuration parameter values search
  Searching and comparing layer affect
Notes: Up to this point we created the running environment without any problem with PID system.
Agent trainig and optimizing reward function trials started and continue but has some problems. Therefore we will solve the training problems soon.
Observation and action block parameters was not limited and should be limited.
We have chosen DDPG and PPO algorithms. These algorithms will be worked together simultaneously in the final version of the project.
Whatever the agent is configuration parameters should be configured. This parameters configure the agent. Therefore, we will search this affects our agents.
Layer affect also another parameter that affect the agent this will be searched. For this now we are using 128? layer.

## Slide 21
Thanks for listening.